## Slide 1: The Art of Troubleshooting: 16 Segment Display
By: Raj Joshi
Teacher: Mr. Paterno

## Slide 2: About the Project
Design a 16 – segment decoder using PLDs
Must decode minimum of 26 letters and 10 digits
Use 2 GAL22v10s since a single chip only has 10 outputs

## Slide 3: Original Procedure
Use premade Excel Spreadsheet to generate equations
Use WINCUPL and equations to generate .JED file
Use WELLON to program PLDs
Simple and Easy
Time: 30 minutes

## Slide 4: 1st Trial
Did not work
Used Oscilloscope to look at output of the function generator  it was good
Cascaded 74ls193 counter chip
  Checked output to see if it worked using a bar graph  it worked
Checked if 16 segment display was working correctly  it was
ISOLATED THE PROBLEM: PLD! 

## Slide 5: PLD – WELLON Diagnostic
Reprogrammed PLD
Changed pin number and then reprogrammed PLD
Replaced the PLD and then program
STILL DID NOT WORK
Conclusion – WELLON was not the cause of the problem

## Slide 6: Digging Deeper
Hunch that something with WINCUPL wasn’t working
Found 2 problems immediately:
  Code would not compile unless WINCUPL minimized equation by itself
  WINCUPL messed up minimized terms

## Slide 7: More Problems
Excel spreadsheet code generation was not working
Looked at Visual Basic Code  Looked Wrong
  Test simple truth table  Failed
Excel spreadsheet was also configured for active high output
  16 – segment display was Active Low

## Slide 8: Final Approach
Using the Excel Spreadsheet, generate a truth table for the Common Anode 16 segment Display
Copy over the truth table to Logic Friday
Use minimizing tool on Logic Friday and Generate Equations
Use python script to change the Logic Friday syntax to CUPL syntax
Use WINCUPL and equations to generate a .JED file
Program PLD using WELLON  (2x GAL22v10)